dmesg:
A command in Unix OS that prints diagnostic messages from the kernel ring buffer, including messages from device drivers.

| (pipe):
Shell operator pipe ( | ), takes output from one command and uses it as input for another

tail:
- command used to display the last part of a file
- by default it outputs the last 10 lines of the specified file

dmesg | tail:
display last 10 lines of diagnostic messages

/dev/tty*
Unix os refers to a family of device special files representing various types of terminals interfaces including, physical serial ports, virtual terminals, usb serial interfaces and teletypewriters

ls
list files in current directory

grep
command line utility used for searching plain-text data sets for lines that match a regular expression

dmesg | grep tty
search diagnostic messages for tty

tty
teletypewriter, used for terminal input/output. Currently used for serial communication

ACM
Abstract Controle Model, part of the USB CDC spec, a common way microcontrollers expose virtual serial ports over usb

ls /dev/tty*
- will display a list of all the teletypewriters, if you have microbit or any micro controler connected should display /dev/ttyACM0
- Where zero is the first device if there are multiple devices this number will increment

lsusb
command lists information about USB devices connected to a linux system

ll
Alias for ls -l, which meas list files in long format

/sys/class/tty
symbolic link to a directory in /sys/devices/… that contains metadata about that device

ll /sys/class/tty/ttyAMC*
Lists detailed metadata about tty devices, such as those created by USB-connected microcontrollers like Microbit. ttyACM0 is one such device if a USB CDC interface is active.

cat
concatenate: Display the contents of a file to the terminal

Microbit product and serial information location and how to read
- ll /sys/class/tty/ttyACM0/device/../
- cat /sys/class/tty/ttyACM0/device/../* (where * is placeholder for information you want idProduct, serial, product, etc)

screen: needs to be installed
screen is a terminal multiplexer, it lets you run a shell session that you can detach, leave running in the background, and reconnect to later.

/dev/tty*
Is a serial device file on Linux that represents a USB-connected serial interface

screen /dev/ttyACM0 115200
Opens a connection to the micro:bit’s serial interface
Uses screen as a terminal emulator
Communicates with /dev/ttyACM0, which is the micro:bit’s USB serial port
Sets the baud rate to 115200 — the speed at which data is transferred over serial

definition: Baud rate – is the number of signal changes per second in a communication channel.
To find baud rates look at the device’s datasheet, user manual, or manufacturer’s website.
Most devices have default baud rates like:
- 9600 (very common)
- 38400, 57600
- 115200 (used by micro:bit, ESP32, many dev boards)
- If the device is a microcontroller or custom firmware, check its code